## Slide 1: DeapLearning appoach for acoustic signals classification
date
Ahmed Ben Sidhom
Electrical and Computer Engineering PhD candidate
Advisor: Dr. Antonios Kontsos
Director, Digital Engineering Hub (DEHub)​
Henry M. Rowan Foundation Professor ​
Dept. of Mechanical Engineering​
Dept. of Electrical Engineering (courtesy)​
Materials Science & Engineering (affiliated)​
Henry M. Rowan College of Engineering (HMRCOE)

## Slide 2: I. Problem Formulation
Setup:
- Steel plate (750 x 750 x 4) mm
- 4 sensors of type VS150-RIC (34 dB gain)
- Acquisition settings:
- Digital filter: bypass -> 85-2400 kHz (analog filter)
- Threshold: 40 dBAE
- Sample rate: 5 MHz
- Pretrigger samples: 2048
- Post-duration samples: 1024

## Slide 3: II. Data Discovery data collection
Four different sources (source mechanisms):
1. Sherbet powder (cavitation): Sherbet powder was applied to the substrate surface (in small piles) and sprinkled with water until a visible reaction took place (bubble formation).
2. Fiber friction (soft on hard): The part with the barbs was used from a commercially available hook and loop fastener and the barbs were brought into contact with the substrate. The hook and loop fastener was then moved in circles over the substrate using variable pressure applied with fingers.
3. Sand (impacts): Sand with a maximum grain size of 1 mm was dropped onto the substrate surface from a height of approx. 20 cm.
4. Sand friction (hard on hard): A small metal plate was passed over the substrate surface. Grains of sand were placed between the metal plate and the substrate.
The data set if balanced with ~6900 records for each source.

## Slide 4: II. Data Discovery Visiualization
Different number of samples

## Slide 5: II. Data Discovery feature extracrion

## Slide 6: II. Data Discovery feature extracrion
Continuous Wavelet transformation:
Scaling: Wavelets can be stretched or compressed, changing their scale. A large scale corresponds to low frequency, capturing slower changes in the signal, while a small scale corresponds to high frequency, capturing quick changes.
Shifting: The wavelet is moved or shifted across the signal to analyze different parts. This shift allows you to study the signal both locally in time and at different resolutions

## Slide 7: III. Approach tabulated data classification
Input
Model
Output
Amplitude
Duration
Energy
RMS
Rise Time
Counts
Sand
Sherbet
fiber
Sand friction

## Slide 8: III. Approach image classification
Input
Model
Output
Sand
Sherbet
fiber
Sand friction

## Slide 9: IV. Data preprocessing Data labeling and splitting
80% training
20% validation

## Slide 10: V. Traoining process tabulated: Hyperparameters finetuning and model evaluation

## Slide 11: V. Training process images: Hyperparameters finetuning and model evaluation

## Slide 12: V. Training process images: Hyperparameters finetuning and model evaluation
Transfer learning

## Slide 13: V. Training process images: Hyperparameters finetuning and model evaluation
Finetuning pretraining model

## Slide 14: VI. results tabulated:
Confusion matrix

## Slide 15: VI. results tabulated:
deplyment
.keras
.onnx
linwave

## Slide 16: V. Results images:
Confusion matrix

## Slide 17: Thank you for your attention! Questions?
kontsos@rowan.edu
bensid28@students.rowan.edu